## Slide 1
Run Your Code on a GPU
From Zero to GPU · Session 2
In one hour you will write a program that changes a photo
using 2,457,600 threads at the same time.
Notes: Welcome back. Last time: you built a tool on a Linux machine. Today is different - today your code runs on a completely different processor, and you'll see a photo change because of it. Housekeeping: get Colab open and switch the runtime to T4 GPU NOW, before we start talking. The first GPU allocation is slow and I want it out of the way.

## Slide 2
Why does everyone want these chips?
Every answer ChatGPT gives you is
thousands of GPU cores doing simple sums.
By the end of the hour you'll have written that same kind of code — the same shape, on a much smaller problem — and you'll know exactly why it has to be a GPU and not the processor you normally use.
Notes: This is the promise for the hour. Don't oversell - be specific: the SHAPE of what they write today is the shape of what runs a model. Don't explain how yet. That's the payoff at the end, and it lands much harder once they've written the code.

## Slide 3
A CPU and a GPU are good at opposite things
CPU
Four brilliant mathematicians
Give them anything — a hard problem, a weird problem, a problem that changes halfway through — and they'll work it out, fast, one step after another.
Ask them to do a million tiny sums and they'll be there all afternoon.
GPU
A stadium of students
Each one can do exactly one small sum, and not quickly.
But there are thousands of them, and if you can hand every single person their own sum at the same moment, they finish together — in the time it takes to do one.
Today's job — “make every pixel in this photo grey” — is two and a half million tiny identical sums.
Notes: Spend real time here. This analogy carries the whole session. The key move is 'identical and independent'. The stadium only wins when every person can start immediately without waiting for anyone else's answer. If sum #2 needs the result of sum #1, the stadium is useless and the mathematicians win. Ask the room: which of these is 'add up these million numbers'? (Trick question - it's partly sequential. Don't dwell, just plant it.)

## Slide 4
The same trade, in numbers
CPU
GPU
How many cores
8 – 16
Thousands
Speed of one core
Very fast
Fairly slow
Best at
Anything, in order
One job, a million times
Memory
Your RAM
Its own, separate
That last row is the one that catches everybody out.
Notes: Move quickly through the first three rows - they're just the analogy made concrete. Stop hard on the last row. Separate memory is the thing that makes CUDA code look the way it does, and if they don't get it now, every cudaMemcpy in the build will look like pointless bureaucracy. Next slide is entirely about that row.

## Slide 5
The catch: the GPU cannot see your data
CPU
your photo
lives here
Ordinary memory. Your program can read and write it whenever it likes.
GPU
its own memory,
completely separate
Thousands of cores can read this at once. Your CPU cannot touch it at all.
copy over
copy back
Two machines in one box, with a cable between them. Nothing the GPU does is visible to you until you ask for it back — and that copying is not free. We'll measure it later.
Notes: The single most useful mental picture in the session. Draw it in the air if you have to. Emphasise: this isn't a rule someone invented, it's physical. They're different chips with different memory attached. Foreshadow the race: 'hold onto the fact that those two arrows cost time. At the end we'll find out that they cost MORE time than the actual work.'

## Slide 6
So every CUDA program does these five things
Leave this on the screen. Every program we write today has exactly this skeleton.
1
Ask the GPU for memory
cudaMalloc(&in_d, bytes);
2
Copy your data over
cudaMemcpy(in_d, img, bytes, cudaMemcpyHostToDevice);
3
Run your code there
myKernel<<<grid, block>>>(out_d, in_d, w, h);
4
Copy the answer back
cudaMemcpy(out, out_d, bytes, cudaMemcpyDeviceToHost);
5
Give the memory back
cudaFree(in_d);
Notes: This is the reference slide. Genuinely leave it up while you code, or duplicate it and come back to it. Point out that step 3 is the only one that's interesting, and it's the only one they'll write today. Steps 1, 2, 4, 5 are already typed in the notebook and never change between the two programs. 'Host' = CPU, 'device' = GPU. That's why it says HostToDevice. Say it once so the constant names stop looking cryptic.

## Slide 7
You don't write a loop. You say how many.
You ask for a number of threads, and they all start at once. But they arrive in fixed-size groups called blocks — so a thread has to work out which piece of the job is actually its own.
block 0
0
0
1
1
2
2
3
3
block 1
0
4
1
5
2
6
3
7
block 2
0
8
1
9
2
10
3
11
small number = threadIdx.x, my seat inside my block large number = the one we actually want: 0 to 11, once each
int col = blockIdx.x * blockDim.x + threadIdx.x;
“Skip past all the blocks in front of me, then add my own seat.” Do it once for across (x) and once for down (y), and a thread knows its pixel.
Notes: THE most important slide before the build. They are about to type this exact line twice and I want it to be familiar, not magic. Walk the diagram: green boxes are threads, small number is threadIdx, big number is what we compute. Note 0..11 with no gaps and no repeats - that's the whole requirement. Two threads with the same number would fight over one pixel; a missing number means a pixel nobody colours. The cinema analogy works well: row number times seats per row, plus your seat. Don't explain WHY blocks exist (shared memory, scheduling). Not today. If asked: 'the hardware hands work out in groups, and there are clever things you can do within a group - that's session three.'

## Slide 8
And a photo is just one long line of numbers
There is no grid in memory. Every row is laid end to end, and every pixel is three bytes: red, green, blue.
row 0
R
G
B
pixel (0,0)
R
G
B
pixel (0,1)
row 1
R
G
B
pixel (1,0)
R
G
B
pixel (1,1)
…
rows just keep going, end to end
int i = (row * width + col) * 3;
“Skip whole rows to get to my row, walk along to my column, then times three because each pixel is three bytes.”
Then i + 0 is red, i + 1 is green, i + 2 is blue. Get row and col the wrong way round here and threads read each other's pixels — it's the classic mistake, and you'll see it if it happens.
Notes: Second of the two lines they're about to type. Same treatment: make it familiar now so typing it isn't mysterious. The 'times three' is worth a beat - beginners often forget the picture is bytes, not pixels. Mention the row/col swap deliberately. When someone does it in the build (someone always does), the notebook says exactly that, and they'll remember hearing it.

## Slide 9
The whole idea, in five words
One thread per
output element.
One pixel, one thread. Two and a half million of them, all at the same moment.
Hold onto this sentence — we're going to use it three times today.
Notes: Say it, then make them say it. It is the thread that ties the pixel work to the LLM payoff at the end. Three uses: one thread per PIXEL (today's build), one thread per NUMBER in a matrix multiply, and that's what a language model is made of. Short slide. Don't linger - go and build something.

## Slide 10
What we're about to build
the photo
1920 x 1280 = 2,457,600 pixels
program 1 — greyscale
each pixel mixes its own colours
program 2 — blur
each pixel averages its neighbours
(zoomed in, or you'd never see it)
Two programs — but the five steps never change between them. The only thing we rewrite is what a single thread does once it knows which pixel it owns.
Notes: Show them the destination before they start typing. It matters - people type with more confidence when they know what it's for. The third image is a CROP, say so, otherwise the blur looks weak. At full size a 7-pixel blur on a 1920-wide photo is genuinely hard to see on a projector. Set the expectation for the build: 'the second program will feel almost free, because we only change the middle.'

## Slide 11
LAPTOPS OPEN
Build 1 — greyscale
Notebook section 2. The bottom of the cell is already written — that's the five steps.
We write the kernel at the top together. About eight lines.
If you lose the thread: open the 🛟 cell underneath, copy it, and you're back with us.
Notes: ~8 minutes. Type in this order, saying why: col -> 'which column do I own' row -> 'same again, downwards' if -> 'we asked for more threads than pixels; leftovers sit still' i -> 'the flat address, from the slide' the weighted sum -> 'and THIS is the only line that's about grey' When you run it, point at the line printing 2,457,600 threads. That number is the moment the room gets it. Then show the picture. Let them enjoy it. Do NOT stop for individual typos. Point at the lifebelt cell and keep going.

## Slide 12
KEEP THEM OPEN
Build 2 — blur
Notebook section 3. Scroll to the bottom of the cell first: it is identical to last time.
Only the kernel changes — walk the square around me, add up the neighbours, divide.
Watch for the edges: a corner pixel has fewer neighbours than a middle one.
Notes: ~10 minutes. Open by scrolling to the bottom of the cell and saying 'look - nothing down here changed. Same five steps, same launch.' That's the lesson, not an aside. The two for-loops are the only genuinely new thing. Say 'radius three means a seven by seven square'. Dwell on dividing by n rather than 49 - it's the one real gotcha, and if someone gets it wrong the check literally says 'the middle is right but the edges are dark'. After it runs: point at the BOTTOM row of the figure, the zoomed crop. Then: everyone change BLUR_SIZE to 15 and re-run. Twenty times the work, still instant. That lands harder than anything you can say.

## Slide 13
NOTHING TO TYPE
How fast was that, really?
Notebook section 4. The same blur, done twice — once as an ordinary loop on the CPU, once on the GPU.
Two numbers to watch: how much faster the blur itself was, and how much faster it was once you count the copying.
Notes: ~5 minutes. Just run it. Get them to read the two speedup numbers out loud before you explain. Then make the point: the blur itself is hundreds of times faster, but counting the copying it's far less - because most of the GPU's time went on moving bytes, not computing. That's the two-memories slide coming back to bite. And it's the answer to 'why does everyone care whether a model FITS on the GPU' - the weights get loaded on once and left there. Numbers vary by machine. On a T4 expect the CPU around 1-3 seconds and the kernel in single-digit milliseconds.

## Slide 14
Now the payoff: it's the same program
Multiplying two matrices is the same shape of code you just wrote. Only the arithmetic in the middle is different.
your blur
col = blockIdx.x*blockDim.x + threadIdx.x;
row = blockIdx.y*blockDim.y + threadIdx.y;
if (col < w && row < h) {
for (neighbours around me)
total += pixel value;
out[...] = total / count;
}
a matrix multiply
col = blockIdx.x*blockDim.x + threadIdx.x;
row = blockIdx.y*blockDim.y + threadIdx.y;
if (col < w && row < h) {
for (k across the row/column)
total += A[..] * B[..];
out[...] = total;
}
Same “which one am I”. Same bounds check. Same loop that adds things up. One thread per output number — for the second time today.
Notes: Put the two side by side and let them look for a few seconds before you say anything. The recognition is the point. This is use #2 of 'one thread per output element'. Don't teach matrix multiplication properly. All they need: each output number is a sum of products, and every output number can be worked out independently of the others. That's the only property that matters.

## Slide 15
And a language model is mostly matrix multiplies
1
Turning words into numbers
a matrix multiply
2
Working out which words matter to each other
two matrix multiplies
3
The big layers in between
the largest matrix multiplies of all
Producing ONE word means billions of these little sums — every one of them independent, every one of them a “one thread per output number” job. Then it does it all again for the next word.
Notes: Use #3 of the one idea, and the moment the title of the series pays off. Keep it honest and vague where you should be: you are NOT teaching transformers. The claim is only that the expensive parts are matrix multiplies, and matrix multiplies are what they just learned to think about. 'Which words matter to each other' = attention, without the jargon. Use the word if the room can take it.

## Slide 16
Put that on the scale of what you just wrote
361 million
additions in the blur
you just wrote
350 billion
operations for ONE word
of a large model
≈ 1,000
of your blurs,
for a single word
The notebook works this out from YOUR machine's actual timing. A real system answers in a few hundredths of a second per word — the gap is engineering, not magic: faster memory, hardware built for exactly this multiply, smaller numbers, and many GPUs at once.
Notes: Run the last cell of the notebook while this is up - it prints these numbers from their own run, which is far better than reading mine. Be honest about the comparison: the blur adds whole numbers, a model multiplies decimals. It's for scale, not a benchmark. The notebook says so too. Say it out loud - a room that catches you overclaiming stops believing the rest. The useful takeaway is the ratio, not the seconds: one word is about a thousand times the work you just watched happen instantly.

## Slide 17
So — why GPUs, and not CPUs?
Not because GPUs are mysteriously fast.
Because this job is millions of identical, independent sums —
and that is the one thing a stadium beats four geniuses at.
You proved it yourself, on a photo, about twenty minutes ago.
Notes: The closing argument. Slow down and let it land. Callback to the stadium is deliberate - it closes the loop opened in the first five minutes. Last line matters: they didn't take your word for it, they measured it.

## Slide 18
What you did in the last hour
✓
Ran your own code on a genuinely different processor
✓
Handed data to a machine that couldn't otherwise see it — and got it back
✓
Pointed 2.4 million threads at 2.4 million pixels, exactly one each
✓
Made a real photo change, twice
✓
Measured it against a CPU, and found where the time actually goes
If you want to keep going
lab/extras/ in the repo — what happens when you forget the copy back, what the bounds check is really protecting you from, and a matrix multiply that gets several times faster purely by changing which memory each thread reads.
Notes: Read the list out. People genuinely underestimate what they just did, and hearing it back is the difference between 'I followed a tutorial' and 'I wrote GPU code'. Point at extras for the one or two who want more. Don't sell it hard. Then: questions. Common ones - 'do I need an NVIDIA GPU?' (for CUDA yes; there are other frameworks), 'is this what PyTorch does?' (yes, underneath - it calls kernels like these, mostly written by NVIDIA).